## Slide 1: The Language of Bits
PROPRIETARY MATERIAL. © 2014 The McGraw-Hill Companies, Inc. All rights reserved. No part of this PowerPoint slide may be displayed, reproduced or distributed in any form or by any means, without the prior written permission of the publisher, or used beyond the limited distribution to teachers and educators permitted by McGraw-Hill for their individual course preparation. PowerPoint Slides are being provided only to authorized professors and instructors for use in preparing for classes using the affiliated textbook. No other use or distribution of this PowerPoint slide is permitted. The PowerPoint slide may not be sold and may not be distributed or be used by any student or any other third party. No part of the slide may be reproduced, displayed or distributed in any form or by any means, electronic or otherwise, without the prior written permission of McGraw Hill Education (India) Private Limited.
Smruti Ranjan Sarangi, IIT Delhi
Computer Organisation and Architecture
PowerPoint Slides
1
Chapter 2 The Language of Bits

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3: Outline
Boolean Algebra
Positive Integers
Negative Integers
Floating-Point Numbers
Strings
3

## Slide 4: What does a Computer Understand ?
Computers do not understand natural human languages, nor programming languages
They only understand the language of bits
Bit
0 or 1
Bit
0 or 1
Word
0 or 1
Byte
0 or 1
0 or 1
0 or 1
0 or 1
8 bits
0 or 1
0 or 1
0 or 1
4 bytes
kiloByte
0 or 1
0 or 1
0 or 1
1024 bytes
megaByte
0 or 1
0 or 1
106 bytes
4

## Slide 5: Review of Logical Operations
A + B (A or B)
A.B ( A and B)
5
A | B | A + B
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1
A | B | A.B
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1

## Slide 6: Review of Logical Operations - II
NAND and NOR operations
These are universal operations. They can be used to implement any Boolean function.
6
A | B | A NOR B
0 | 0 | 1
1 | 0 | 0
0 | 1 | 0
1 | 1 | 0
A | B | A NAND B
0 | 0 | 1
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0

## Slide 7: Review of Logical Operations
XOR Operation : (A B)
7
A | B | A XOR B
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0

## Slide 8: Review of Logical Operations
NOT operator
  Definition: 0 = 1, and 1 = 0
  Double negation: A = A, NOT of (NOT of A) is equal to A itself
OR and AND operators
  Identity: A + 0 = A, and A.1 = A
  Annulment: A + 1 = 1, A.0 = 0
8

## Slide 9
Idempotence: A + A = A, A.A = A, The result of computing the OR and AND of A with itself is A.
Complementarity: A + A = 1, A.A = 0
Commutativity: A + B = B + A, A.B = B.A, the order of Boolean variables does not matter
Associativity: A+(B+C) = (A+B)+C, A.(B.C) = (A.B).C, similar to addition and multiplication.
Distributivity: A.(B + C) = A.B + A.C, A+ (B.C) = (A+B). (A+C)  Use this law to open up parantheses and simplify expressions

## Slide 10: De Morgan's Laws
Two very useful rules
10
A + B = A.B
A.B = A + B

## Slide 11: Consensus Theorem
Prove :
  X.Y + X.Z + Y.Z = X.Y + X.Z
11

## Slide 12: Outline
Boolean Algebra
Positive Integers
Negative Integers
Floating Point Numbers
Strings
12

## Slide 13: Representing Positive Integers
Ancient Roman System
Issues :
  There was no notion of 0
  Very difficult to represent large numbers
  Addition, and subtraction (very difficult)
13
Symbol | I | V | X | L | C | D | M
Value | 1 | 5 | 10 | 50 | 100 | 500 | 1000

## Slide 14: Indian System
Uses the place value system
Bakshali numerals, 7th century AD
5301 = 5 * 103 + 3 * 102 + 0 * 101 + 1*100
Example in base 10
14

## Slide 15: Number Systems in Other Bases
Why do we use base 10 ?
  because ...
15

## Slide 16: What if we had a world in which ...
People had only two fingers.
16

## Slide 17: Binary Number System
They would use a number system with base 2.
Number in decimal
Number in binary
5
101
100
1100100
500
111110100
1024
10000000000
17

## Slide 18: MSB and LSB
MSB (Most Significant Bit)  The leftmost bit of a binary number. E.g., MSB of 1110 is 1
LSB (Least Significant Bit)  The rightmost bit of a binary number. E.g., LSB of 1110 is 0
18

## Slide 19: Hexadecimal and Octal Numbers
Hexadecimal numbers
  Base 16 numbers – 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
  Start with 0x
Octal Numbers
  Base 8 numbers – 0,1,2,3,4,5,6,7
  Start with 0
19

## Slide 20
Examples
Convert 110010111 to the octal format : = 0627
Convert 111000101111 to the hex format : = 0xE2F

## Slide 21: Outline
Boolean Algebra
Positive Integers
Negative Integers
Floating Point Numbers
Strings
21

## Slide 22: Representing Negative Integers
Problem
  Assign a binary representation to a negative integer
  Consider a negative integer, S
  Let its binary representation be : xnxn-1….x2x1 (xi=0/1)
  We can also expand it to represent an unsigned, +ve, number, N
  If we interpret the binary sequence as :
    An unsigned number, we get N
    A signed number, we get S
22

## Slide 23
  We need a mapping :
    F : S → N (mapping function)
    S → set of numbers (both positive and negative – signed)
    N → set of positive numbers (unsigned)
Set of +ve
numbers
Set of
+ve and -ve
numbers
mapping
23

## Slide 24: Properties of the Mapping Function
Preferably, needs to be a one to one mapping
All the entries in the set, S, need to be mapped
It should be easy to perform addition and subtraction operations on the representation of signed numbers
Assume an n bit number system
SgnBit(u) = 1 , u < 0
0 , u >= 0
24

## Slide 25: Sign-Magnitude Base Representation
Examples :
  -5 in a 4 bit number system : 1101
  5 in a 4 bit number system : 0101
  -3 in a 4 bit number system : 1011
sign bit
|u|
25

## Slide 26: Problems
There are two representations for 0
  000000
  100000
Addition and subtraction are difficult
The most important takeaway point :
  Notion of the sign bit
26

## Slide 27: 1's Complement Representation
Examples in a 4 bit number system
  3 → 0011
  -3 → 1100
  5 → 0101
  -5 → 1010
27

## Slide 28: Problems
Two representations for 0
  0000000
  1111111
Easy to add +ve numbers
Hard to add -ve numbers
Point to note :
  The idea of a complement
28

## Slide 29: Bias Based Approach
Consider a 4 bit number system with bias equal to 7
  -3 → 0100
  3 → 1010
F(u+v) = F(u) + F(v) – bias
Multiplication is difficult
29

## Slide 30: The Number Circle
Clockwise: increment
Anti-clockwise: decrement
0000 (0)
0001 (1)
0010 (2)
0100 (4)
0011 (3)
0111 (7)
1000 (8)
0101 (5)
0110 (6)
1100 (12)
1011 (11)
1101 (13)
1001 (9)
1010 (10)
1110 (14)
1111 (15)
Increment
30

## Slide 31: Number Circle with Negative Numbers
break point
0000 (0)
0001 (1)
0010 (2)
0100 (4)
0011 (3)
0111 (7)
1000 (-8)
0101 (5)
0110 (6)
1100 (-4)
1011 (-5)
1101 (-3)
1001 (-7)
1010 (-6)
1110 (-2)
1111 (-1)
Increment
31

## Slide 32: Using the Number Circle
To add M to a number, N
  locate N on the number circle
  If M is +ve
    Move M steps clockwise
  If M is -ve
    Move M steps anti-clockwise, or 2n – M steps clockwise
  If we cross the break-point
    We have an overflow
    The number is too large/ too small to be represented
32

## Slide 33: 2's Complement Notation
F(u) is the index of a point on the number circle. It varies from 0 to 2n - 1
Examples
  4 → 0100
  -4 → 1100
  5 → 0101
  -3 → 1101
33

## Slide 34: Properties of the 2's Complement Notation
Range of the number system :
  -2(n-1) to 2n-1 – 1
There is a unique representation for 0 → 000000
msb of F(u) is equal to SgnBit(u)
  Refer to the number circle
  For a +ve number, F(u) < 2(n-1). MSB = 0
  For a -ve number, F(u) >= 2(n-1). MSB = 1
34

## Slide 35: Properties - II
Every number in the range [-2(n-1),2(n-1) – 1]
  Has a unique mapping
  Unique point in the number circle
a ≡ b → (a = b mod 2n)
≡ means same point on the number circle
F(-u) ≡2n – F(u)
  Moving F(u) steps counter clock wise is the same as moving 2n – F(u) steps clockwise from 0
35

## Slide 36: Prove : F(u+v) ≡ F(u) + F(v)
Start at point u
  Its index is F(u)
  If v is +ve,
    move v points clockwise. We arrive at F(u+v).
    Its index is equal to (F(u) + v) mod 2n.
    Since v = F(v), we have F(u+v) = ( F(u) + F(v) ) mod 2n
36

## Slide 37: Prove : F(u+v) ≡ F(u) + F(v)
  If v is -ve,
    move |v| points anti-clockwise.
    Same as moving 2n – |v| points clockwise.
    We arrive at F(u+v).
    F(v) = 2n -|v|
    The index – F(u+v) – is equal to:
      (F(u) + 2n – |v|) mod 2n= (F(u) + F(v)) mod 2n
37

## Slide 38: Subtraction
F(u-v) ≡ F(u) + F(-v)
≡ F(u) + 2n - F(v)
Subtraction is the same as addition
Compute the 2's complement of F(v)
38

## Slide 39: Prove that :
Prove that :
F(u*v) ≡ F(u) * F(v)
39

## Slide 40: Computing the 2's Complement
2n – u
  = 2n – 1 - u + 1
  = ~u + 1
  ~u (1's complement)
1's complement of 0100 2's complement of 0100
1111
0100
1011
1011
0001
1100
40

## Slide 41: Sign Extension
Convert a n bit number to a m bit 2's complement number (m > n)
+ve
  Add (m-n) 0s in the msb positions
  Example, convert 0100 to 8 bits → 0000 0100
-ve
  F(u) = 2n – |u| (n bit number) system
  Need to calculate F'(u) = 2m -|u|
41

## Slide 42: Sign Extension - II
2m – u – (2n – u)
= 2m – 2n
= 2n + 2(n+1) + … + 2(m-1)
= 11110000
n
m-n
F'(u) = F(u) + 2m – 2n
42

## Slide 43: Sign Extension - III
To convert a negative number :
  Add (m-n) 1s in the msb positions
In both cases, extend the sign bit by :
  (m-n) positions
43

## Slide 44: The Overflow Theorem
Add : u + v
If uv < 0, there will never be an overflow
Let us go back to the number circle
  There is an overflow only when we cross the break-point
If uv = 0, one of the numbers is 0 (no overflow)
If uv > 0, an overflow is possible
44

## Slide 45: Number Circle: uv < 0
0
1
2
3
-1
-2
-3
-4
u=1
v=-4
45

## Slide 46: Number Circle: uv > 0
0
1
2
3
-1
-2
-3
-4
u=1
v=3
overflow
46

## Slide 47: Conditions for an Overflow
uv <= 0
  Never
uv > 0 ( u and v have the same sign)
  The sign of the result is different from the sign of u
47

## Slide 48: Outline
Boolean Algebra
Positive Integers
Negative Integers
Floating-Point Numbers
Strings
48

## Slide 49: Floating-Point Numbers
What is a floating-point number ?
  2.356
  1.3e-10
  -2.3e+5
What is a fixed-point number ?
  Number of digits after the decimal point is fixed
  3.29, -1.83
49

## Slide 50: Generic Form for Positive Numbers
Generic form of a number in base 10
Example :
  3.29 = 3 * 100 + 2*10-1 + 9*10-2
50

## Slide 51: Generic Form in Base 2
Generic form of a number in base 2
Number
Expansion
0.375
2
–2
+2
1
2
0
1.5
2
0
+2
–1
2.75
2
1
+2
–1
+2
–2
17.625
2
4
+2
0
+2
–1
+2
–3
–3
51

## Slide 52: Binary Representation
Take the base 2 representation of a floating-point (FP) number
Each coefficient is a binary digit
Number
Expansion
BinaryRepresentation
0.375
2 + 2
–2 –3
0.011
1
2
0
1.0
1.5
1.1
2.75
10.11
17.625
10001.101
2 +2
1 –1
+ 2
-2
2 +2
4 0
+ 2 +2
–1 -3
20 + 2–1
52

## Slide 53: Normalized Form
Let us create a standard form of all floating point numbers
S → sign bit, P → significand
M → mantissa, X → exponent, Z → set of integers
53

## Slide 54: Examples (in decimal)
1.3827 * 1e-23
  Significand (P) = 1.3827
  Mantissa (M) = 0.3827
  Exponent (X) = -23
  Sign (S) = 0
-1.2*1e+5
  P = 1.2 , M = 0.2
  S = 1, X = 5
54

## Slide 55: IEEE 754 Format
General Principles
  The significand is of the form : 1.xxxxx
  No need to waste 1 bit representing (1.) in the significand
  We can just save the mantissa bits
  Need to also store the sign bit (S), exponent (X)
55

## Slide 56: IEEE 754 Format - II
sign bit – 0 (+ve), 1 (-ve)
exponent, 8 bits
mantissa, 23 bits
1
8
Sign(S)
Exponent(X)
Mantissa(M)
23
56

## Slide 57: Representation of the Exponent
Biased representation
  bias = 127
  E = X + bias
Range of the exponent
  0 – 255 ⟷ -127 to +128
Examples :
  X = 0, E = 127
  X = -23, E = 104
  X = 30 , E = 157
57

## Slide 58: Normal FP Numbers
Have an exponent between -126 and +127
Let us leave the exponents : -127, and +128 for special purposes.
58

## Slide 59
What is the largest +ve normal FP number ?
What is the smallest –ve normal FP number ?
59

## Slide 60: Special Floating Point Numbers
NAN + x= NAN 1/0 = ∞
0/0 = NAN -1/0 = -∞
sin-1(5) = NAN
E
M
Value
255
0
 if S = 0
255
0
255
 0
NAN(Not a number)
0
0
0
0
Denormal number
 0
–  if S = 1
60

## Slide 61: Denormal Numbers
Should this code print ''error'' ?
How to stop this behaviour ?
f = 2^(-126);
g = f/2;
if (g == 0)
print ("error");
61

## Slide 62: Denormal Numbers - II
Significand is of the form : 0.xxxx
E = 0, X = -126 (why not -127?)
Smallest +ve normal number : 2-126
Largest denormal number :
  0.11...11 * 2-126 = (1 – 2-23)*2-126
              =2-126 - 2-149
62

## Slide 63
Example
Find the ranges of denormal numbers.
Answer
For positive denormal numbers, the range is [2-149 , 2-126 – 2-149 ]
For negative denormal numbers, the range is [-2-149 , -2-126 + 2-149 ]

## Slide 64: Denormal Numbers in the Number Line
Extend the range of normal floating point numbers.
0
Denormal numbers
Normal FP numbers
64

## Slide 65: Double Precision Numbers
Approximate range of doubles
  ± 21023 = ± 10308
  This is a lot !!!
Field
Size(bits)
S
1
E
11
M
52
65

## Slide 66: Floating Point Mathematics
C will be computed to be 0
  There is no way of representing A+B in the IEEE 754 format
A smart compiler can reorder the operations to increase precision
Floating point math is approximate
A = 2^(50);
B = 2^(10);
C = (B+A)- A;
66

## Slide 67: Outline
Boolean Algebra
Positive Integers
Negative Integers
Floating Point Numbers
Strings
67

## Slide 68: ASCII Character Set
ASCII – American Standard Code for Information Interchange
It has 128 characters
First 32 characters (control operations)
  backspace (8)
  line feed (10)
  escape (27)
Each character is encoded using 7 bits
68

## Slide 69: ASCII Character Set
Character
Code
Character
Code
Character
Code
a
97
A
65
0
48
b
98
B
66
1
49
c
99
C
67
2
50
d
100
D
68
3
51
e
101
E
69
4
52
f
102
F
70
5
53
g
103
G
71
6
54
h
104
H
72
7
55
i
105
I
73
8
56
j
106
J
74
9
57
k
107
K
75
!
33
l
108
L
76
#
35
m
109
M
77
$
36
n
110
N
78
%
37
o
111
O
79
&
38
p
112
P
80
(
40
q
113
Q
81
)
41
r
114
R
82
*
42
s
115
S
83
+
43
t
116
T
84
,
44
u
117
U
85
.
46
v
118
V
86
;
59
w
119
W
87
=
61
x
120
X
88
?
63
y
121
Y
89
@
64
z
122
Z
90
^
94
69

## Slide 70: Unicode Format
UTF-8 (Universal character set Transformation Format)
  UTF-8 encodes 1,112,064 characters defined in the Unicode character set. It uses 1-6 bytes for this purpose. E.g.अ आ क ख, ௹ᇜಞஸ
  UTF-8 is compatible with ASCII. The first 128 characters in UTF-8 correspond to the ASCII characters. When using ASCII characters, UTF-8 requires just one byte. It has a leading 0.
  Most of the languages that use variants of the Roman script such as French, German, and Spanish require 2 bytes in UTF-8. Greek, Russian (Cyrillic), Hebrew, and Arabic, also require 2 bytes.
70

## Slide 71: UTF-16 and 32
Unicode is a standard across all browsers and operating systems
UTF-8 has been superseded by UTF-16, and UTF-32
UTF-16 uses 2 byte or 4 byte encodings (Java and Windows)
UTF-32 uses 4 bytes for every character (rarely used)
71

## Slide 72
72
THE END