## Slide 1: ELL 304 Analog Electronic Circuits
Section A: Instructor: Rakesh Kumar Palani
Ex-Chair, IEEE CAS CSS Delhi Chapter
Assistant Professor
Department of Electrical Engineering
Indian Institute of Technology, Delhi
Hauz Khas, New Delhi 110016

## Slide 2: Why Analog is interesting?
Analog design is art and science at the same time.
Art  It requires creativity to strike the right compromises between the specifications imposed
Science  It requires a certain level of methodology to carry out a design
-- Wiley Sansen

## Slide 3: Why Analog is interesting?
There is not one solution to a problem
  Each one can arrive at same solution via different routes
  It depends on the creativity of individuals

## Slide 4: Why do we need Analog?
World is analog, unless you look at quantum levels
All signals by nature is analog
  Some signal conditioning is done in analog before A-D
  All processing in done in digital
  Signal transmitted back to world in analog
An example

## Slide 5: ELL 304 Course Structure
Class Timing F slot, Tu/W/F 11-12 pm.
  Section-A WS-101 (G1-G4), Instructor : Rakesh Palani
  Section-B VI-LT1 (G5-G8). Instructor : Ankesh Jain
Tutorial:
  LH 613: 1-2 pm, Mon G1-G2, Tue G3-G4
  LH 602: 1-2 pm, Thu G5-G6, Fri G7-G8
Lab :
  II 401: 2-5 pm, Mon G1-G2, Tue G3-G4
  II 401: 2-5 pm, Thu G5-G6, Fri G7-G8
Reference:
  Behzad Razavi, Design of Analog CMOS integrated Circuits

## Slide 6: ELL 304 Grading
Lab: 40 points
  There will be 6 labs
    24 points is for report +viva and 16 points is Quiz on the lab
Tutorial: 10 points
  Each Tutorial  one quiz and the best 10 Quiz will be counted
Assignment: 20 points
  5 Assignments  Best 4 will be counted
Project: 10 points
Minor: 25 points
Major : 35 points
Theory:100 Points
Lab : 40 points
Total :140 points

## Slide 7: ELL 304 Honor Code
Cheating in any form will incur serious penalities
  Remember grading is relative
  Found in any tutorial, lab or exams will result in 0 point
  Remaining portion of the grade will be scaled by 50%
    For eg found cheating once in tutorial 1
      Your score = 0 in tut1 +0.5(score of remaining tutorials)
      Report to DISCO, IIT Delhi
      Second time cheating in tutorial say 5
      Your score = 0 in tut1+ 0 in tut5 + 0.25(score of remaining tutorials)
We will trust you and we will try not to tempt you
Try not to place us in this unpleasant situation

## Slide 8: Syllabus
Motivation to amplifiers
Need nonlinearity for amplification
Introduction to MOSFETs
Small signal approximation
Biasing
Current Mirror
Single stage amplifiers
Introduction to Differential pair
We will deal only with MOSFETs and not BJTs unless necessary

## Slide 9: Some conventions
Highest potential is typ. power supply
Lowest potential is ground
Current flowing into element is positive
If Z is passive VI >0
If Z is active, eg battery VI<0
Voltages are typically measured wrt gnd
  Its indicated as V1 in the figure

## Slide 10: Passivity
If the two port is passive
  V1I1 + V2I2 >0
  This cannot generate power
  Input power Pin = V1I1
  Output power Pout = -V2I2
  Pin > Pout
Its evident that the
  two port is lossy
  It is passive
  Output power is lower than Input power
  Power amplification is not possible with passive network

## Slide 11: Puzzle - 1
Current at resonance freq = Vin/R
Voltage across C  I/ωC  Vin /(ωRC)
; Vo =  Qvin
> 1, ; Voltage and Power amplification
What are we missing ?

## Slide 12: Need for nonlinearity
Take the extra power from the Power supply Vdc
Convert this power to the power at input freq
Linearity
  Superposition
  Scaling
DC power will appear only at dc if network is linear
Non linearity is needed for power amplification
  V1 =Asinωt ; V2 =kAsin(ωt+φ) ; k>1
  Dc power has to be translated to frequency ω

## Slide 13: Small Signal Analysis
Nonlinear Theory and Analysis
  Its complicated and its hard to get intuition
  Lets do a small signal approximation
If the input signal is less than operating point
  Linearize the function around operating point
  Apply linear theory for analysis
  y 

## Slide 14: Introduction to Diodes
PN Junction
  Needed for rectifiers to charge battery in cell phone
  This is the simplest architecture to study
  If the junction formed at t=0.
  Equilibrium is reached
    Electric field stops diffusion current

## Slide 15: Drift and Diffusion current
(Electron move opp to E)
(q is negative for holes)
J_tot = +)q E

## Slide 16: Diffusion current
Charge move from higher to lower concentration
  Analogous to ink diffusing in a cup of water
*https://www.easybiologyclass.com/difference-between-diffusion-and-osmosis-a-comparison-table/

## Slide 17: Diffusion current
Charge move from higher to lower concentration
  Analogous to ink diffusing in a cup of water
A is cross section area, Q is charge and dn/dx is the gradient, D is the diffusion constant
*https://www.easybiologyclass.com/difference-between-diffusion-and-osmosis-a-comparison-table/

## Slide 18: Diode Equation
For the derivations of diode equations refer
http://www.faculty.jacobs-university.de/dknipp/c300331/Lectures/4%20Diodes.pdf
Diode in Forward bias
Where Ln and Lp are electron and hole diffusion length
For course we just need this eqn

## Slide 19: Small Signal Analysis: Motivation
We need to find ID
ID is a function of Vin
Need to solve this nonlinear equation with Vin
  Quite cumbersome
  LHS is red, RHS is blue
  Point of intersection is solution
  When Vin is changed by δ, red curve is shifted
  Actual solution involves solving this non linear equation again

## Slide 20
Small Signal Analysis: Motivation
We need to find ID
ID is a function of Vin
Need to solve this nonlinear equation with Vin
  Quite cumbersome
  Linearize around operating point
  Find the approximate solution
  Accuracy depends on the value of δ

## Slide 21: Some Approximations
Approximations
Forward bias
  V>VT ,
  Voltage across diode is pinned to VF
  If I changes by 2x, V ~VT ln(2) 18mV
  Operating voltage ~700mV
  Diode Voltage ~700mV for all currents
Reverse Bias
  Current is ~Is << Forward bias current
  Current is approximated to zero

## Slide 22: Example -1
Iin = 3mA.
  A sinusoidal signal of 100u(sinwt) is applied with Iin.
Calculate the amplitude of sinusoidal wave at Vout?
Assume diode drop is 0.8V

## Slide 23: Example -1
Operating point at Vout is 0.8V (diode drop)
Current is diode is 2.6mA and R2 is 0.8/2k =0.4mA
Small signal diode res. is VT/Id2 = 26m/2.6m =10 ohm
Vout = 100usin(wt) * (2k||10) ~ sin(wt) mV

## Slide 24: Example -2
Vin = 4.2V.
  A sinusoidal signal of sinwt is applied with Vin.
Calculate the amplitude of sinusoidal wave at Vout?
Assume diode drop is 0.8V

## Slide 25: Example -2
I =(vin-1.6)/1k =2.6mA
Small signal diode res. is VT/Id2 = 26m/2.6m =10 ohm
Vout = sin(wt) * (1010/1020) ~ 0.99sin(wt)

## Slide 26: Small Signal equivalent
1 ensures passivity, if V=0 I=0
If diode is forward biased e(V/VT) >>1
or
Small signal Equivalent of diode is a Resistor of value VT/I
VT is thermal voltage (kT/q) ~ 26mV @27C
Expanding in Taylor series,

## Slide 27: Diode
Applications
  Half wave and Full Wave Rectifier
  Limiting Circuits
  Voltage Doublers
  Level Shifters
Not going through details of these applications in this course. Ref chapter 3 in Text book if you want to learn more

## Slide 28: Diode as Logic gate
AND/OR Gate are possible with diodes
But inversion is not possible
  Current increases with applied voltage
Hence universal gates not possible
We need a device where increasing voltage reduces current.
  Means a negative resistance in 1 port (not possible)
  we need 2 port where voltage reduces current in other port
    Three terminal device needed

## Slide 29: Summary
Amplification
  We need Non-Linearity
  Small Signal Analysis
    Linearize IV characteristics near operating point
    Use Linear theory
  Diode
    Two terminal device
    Current flows only in one direction
    Small signal Equivalent is a resistor
    NOT gate is not possible using diodes
  Three terminal device
    Uses PDC to amplify PIN

## Slide 30: Introduction to Two port
Ideally two port network has separate terminals for input and output
For amplifier design we have one terminal common
  For simplicity
  Three terminal two port model
Two port Model
Three terminal Two port Model

## Slide 31: Three terminal Two Port
Three terminal Two port Model
Apply the same small signal analysis
  Change in V1 and V2 by ∆
Evaluated at operating points

## Slide 32: Three terminal Two Port
Three terminal Two port Model
Apply the same small signal analysis
  Change in V1 and V2 by ∆
Evaluated at operating points
Unit of conductance

## Slide 33: Three terminal Two Port
y11- Effect of port 1 on port 1
y12- Effect of port 2 on port 1
y22- Effect of port 2 on port 2
y21- Effect of port 1 on port 2
Three terminal Two port Model
I1, I2 and V1,V2 are small signal parameters

## Slide 34: Condition for maximum gain
Source has output impedance of RS and load is RL
Gain =
Maximize y21
Minimize denominator
  y22, y11 are positive conductances, min =0
  Y21 is the effect of V2 on I1. Looks positive feedback
    Y12 =0 to get unconditional stability

## Slide 35: Condition for maximum gain
1.
2. Maximize y21
Y11 = 0; Input loading =0
Y22 = 0; Output loading =0
Y12 = 0; Breaks feedback
Y21 ; Converts input voltage to output current, maximize

## Slide 36: Introduction to MOSFETs
Its basically a capacitor
When gate potential is zero
  Channel has holes
  The channel between source and drain is cut off
When gate potential is high
  Electrons are attracted to surface forming a channel
MOSFET Structure

## Slide 37: N-MOSFET
It’s a 4 terminal device (NMOS)
Channel is n-type, bulk is p-type
Assume bulk is connected to lowest supply
  We will deal with bulk little later
Gate is a high impedance node, IG ~ 0
  IG ~ 0
Source and Drain is interchangeable
Symbol

## Slide 38: P-MOSFET
It’s a 4 terminal device
Channel is p-type, bulk is n-type
Assume bulk is connected to highest supply
  We will deal with bulk little later
Gate is a high impedance node, IG ~ 0
  IG ~ 0
Source and Drain is interchangeable
Symbol

## Slide 39: MOSFET Equations (NMOS)
MOSFET is on
  VGS >VT
  VT is the threshold voltage
VGS > VT ; VGD <VT ; (Saturation Region )
VGS > VT ; VGD >VT ; (Linear Region )
MOSFET Structure
For derivations refer chapter 6 in Text book

## Slide 40: MOSFET Equations (PMOS)
MOSFET is on
  VGS >VT
  VT is the threshold voltage
VSG > VT ; VDG <VT ; (Saturation Region )
VGS > VT ; VGD >VT ; (Linear Region )
P MOSFET
For derivations refer chapter 6 in Text book

## Slide 41: Id-VGS characteristics
Here we do for NMOS
  You will repeat it for PMOS in your lab -1
Vds =50mV -1.8V
Vds =50mV -1.8V
VT ~ 450mV -1.8V
Condition for Saturation
VGD <VT, VGS >VT
VG –VD < VT
Drain can be lower than gate by a threshold voltage
Linear
Region
Saturation Region

## Slide 42: Id-VDS characteristics
Here we do for NMOS
  You will repeat it for PMOS in your lab -1
Vgs =100mV -1.8V
Condition for Saturation
VGD <VT, VGS >VT
VG –VD < VT
Drain can be lower than gate by a threshold voltage
Triode
Saturation
Sub-threshold
Output impedance

## Slide 43: Lets revisit y parameter
We saw for maximal amplification
  Y11 = 0, Y22 = 0, Y12 = 0, Maximize (Y21)
  Input impedance of MOS is high, Y11 = 0
  If we ignore caps Y12 = 0
    MOS is gate controlled device
Condition for Maximal amplification

## Slide 44: Id-VGS characteristics
Condition for Saturation
VGD <VT, VGS >VT
VG –VD < VT
Drain can be lower than gate by a threshold voltage
Linear
Region
Saturation Region
Y21
Maximize Y21
Maximum Y21 is obtained when the transistor goes to saturation region !
Y21 increase

## Slide 45: Id-VDS characteristics
Condition for Saturation
VGD <VT, VGS >VT
VG –VD < VT
Drain can be lower than gate by a threshold voltage
Saturation
Y22
Triode
Y22 ~0
A MOSFET in saturation gives Y22 ~0
It can be used as amplifier when biased here!

## Slide 46: For maximizing gain
Gate current = 0
Output conductance = 0; gds =0
Maximize Transconductance; maximize gm
Y12 =0; For unconditional stability
Transistor should be operated in saturation to satisfy these conditions

## Slide 47: Small Signal Analysis
MOSFET
  Drain current is a function of both gate and drain voltage
  Lets find incremental current for small changes in VGS and VDS
Unit is conductance, but its port 2 current by port 1 voltage. So termed as transconductance
Unit is conductance, but its port 2 current by port 2 voltage. So termed as output conductance

## Slide 48: Small Signal: Transistor (Saturation)
(Ignore λ for simplicity)
(gm in terms of W/L and overdrive)
(gm in terms of W/L and drain current)
(gm in terms of overdrive voltage and drain current)
(Mobility of electrons)
(Oxide Capacitance per unit area)
(Gate width and Length)
(Overdrive voltage, Vdsat)
(How much gate voltage we have more than threshold)

## Slide 49: Small Signal: Transistor (Saturation)
(Ignore λ for simplicity)
Slope is gm, Maximize for higher gain

## Slide 50: Small Signal: Transistor (Saturation)
(Ignore λ for simplicity)
Saturation
Slope is gds, Ideally we want to be zero

## Slide 51: Small Signal Analysis (NMOS)
NMOS is in saturation
  Summary
Transconductance different forms
Output conductance
Output impedance

## Slide 52: Small Signal Analysis (Triode)
Drain voltage is lesser than VG-VT.
gm is lower than gds for the transistor in triode
  Gate has lower control than drain on channel
  gds for transistor in triode is approx. same as gm of transistor in saturation.
Condition for Triode
VGD >VT, VGS >VT
VG –VT > VD

## Slide 53: Small Signal Analysis (Triode)
The slope is the gds
gds,sat < gds,triode
gm,sat > gm,triode

## Slide 54: Small Signal Analysis
Gate has more control on channel (Saturation)
Drain has more control on channel (Triode)
Transistor in Triode
  Is a resistor whose value depends on VGS
Transistor in Saturation
  Is a current source whose value depends on VGS
gds,sat < gds,triode
gm,sat > gm,triode

## Slide 55: Tutorial
Derive the small signal parameters for PMOS Transistor

## Slide 56: Condition for maximum gain
1.
2. Maximize y21
Y11 = 0; Input loading =0
Y22 = 0; Output loading =0
Y12 = 0; Breaks feedback
Y21 ; Converts input voltage to output current, maximize

## Slide 57: Body Terminal
Body/Bulk terminal
  Nmos
    Bulk is connected to gnd
  Pmos
    Bulk is connected to highest supply
Forward biasing the bulk diode will reduce threshold voltage
This is sometimes considered as back gate
Small signal approximate current is gmbVbs

## Slide 58
Gate is a high impedance node. Y11 ~0.
Voltage controlled current source (gmVgs) = Y21 Vgs
Output conductance gds. Y22 = gds. Ideally zero
There is no Y12.
Small Signal Model (dc)
Small Signal Model of MOS to be used as amplifier

## Slide 59: MOSFET Capacitors
Capacitances from every node to every other node
CGS and CGD are the gate to source and drain capacitors
  They consist of overlap capacitor
CDB and CSB are the reverse bias junction caps
Transistor in Saturation
Transistor in Triode

## Slide 60: Biasing
MOSFETs has to be biased
  In saturation to be used as amplifier
  In Triode to be used as resistor
Biasing
  Constant voltage biasing
  Constant current biasing
  Constant trans-conductance (gm) biasing
  So on…

## Slide 61: Why biasing is important
The transistor Id-Vgs is expansive in nature
  This feature gives gain
  The transistor threshold voltage, temperature, process corners etc can create a change in the charactristics
Constant Voltage Biasing
  Lets say transistor Vgs is always Vb
  If VT changes by ∆VT
    ∆Ids will be large due to expansive nature

## Slide 62: Why biasing is important
Typically transistors are biased using constant current in all amplifiers
Constant Current Biasing
  Lets say transistor Vgs is always Vb
  If VT changes by ∆VT
    ∆Vgs will be small due to expansive nature

## Slide 63: Const. Voltage biasing
The resistor Rs reduces the sensitivity of Ids with the threshold voltage

## Slide 64: LT Spice Schematic

## Slide 65: LT Spice Results
Variation reduced from 40% to 27%

## Slide 66: Self-Bias

## Slide 67: Single Stage Amplifiers